## Slide 1: Hong Kong Octopus System
Technology applied in the use
of the Octopus Card
WY Lee
Development Manager
Creative Star Ltd

## Slide 2: Contents
Brief History and Current Status
Card Technology
Applications
System Architecture
Future Plan and Conclusion

## Slide 3: Timeline
First concepts – 1992
JV Shareholders agreement – 1994
Contract award to system integrator – 1994
Sony Card selected – 1995
Public launch – Sep 1997
Deposit taking company – 2000
6m daily transactions – Nov 2000

## Slide 4: The Organization
Creative Star Limited – established in 1994
Service Providers
  New World First Bus New World First Ferry
  NW Telecom HKUST Bus
  HKTel Hongkong & Kowloon Ferry
  Kwoon Chung Bus Chung Tung Minibus
  New Lantau Bus HKR Airport Ferry
  Aberdeen Maxicab Star Ferry
  Swire CoCa Cola Maxim Fast Food
  7-Eleven Vitaland School Shops
  Wilson parking Starbucks

## Slide 5: Current Status
More than 7 million cards + watches
Average daily transactions around 5.6 million
HK$40 million in transaction value per day
40+ Service Providers
Over 15,000 devices in the field
91% economically active population penetration

## Slide 6: Card Technology
Sony Contactless Smart Card Technology
Radio Waves 13.56MHz
Communication Speed: 211Kbps
Memory: EPROM 16bytes x 96 blocks

## Slide 7: Contactless Smart Cards - How they work
Application Specific IC
Memory
Radio
Transceiver
RISC
Antenna

## Slide 8: Octopus watch
Small antenna
Non-metallic case
Other wearables

## Slide 9
Personalized Octopus
Mandatory for Autopay
Used as Staff ID
Loyalty Schemes
Student Concessions
350,000 Issued
Different data stored in card to identify concession, staff, bonus points, autopay etc.

## Slide 10: Contactless Smartcard Readers
Reader/Writer
Distance: 100mm / 20mm
Transaction time: < 300ms
CPU: 32bit with RAM and Flash
Interface: RS232C or RS485

## Slide 11: Encryption
Fast symmetric encryption
  Same keys for encryption and decryption
Dynamic keys
Different keys for different areas
Mutual authentication (R/W and Card)
  RW sends KA(RA) and expects KB(RA)
  Card sends KB(RB) and expects KA(RB)
  Subsequent messages encrypted by RB

## Slide 12: Octopus Processor
Sony Reader/writer inside
Embedded microprocessor system
Tailored for the particular application
Gates
Bus unit
Platform unit
Enquiry unit
Office unit
Portable unit
Minibus unit
Vending machine unit
Retail unit
Access Control unit
Parking Meter
Add value machine

## Slide 13: Passenger Gate
Controls also magnetic ticket and turnstile
Connected to station computer

## Slide 14: Peak Tram

## Slide 15: Buses
Driver control unit
Route selection
Sectional fare
Driver sign-on card
Wireless LAN connecting to Depot computer
Fare table/ config/ programs can be updated via wireless LAN

## Slide 16: PLB Operations

## Slide 17
Light Rail
Platform processors acting as:
  Entry processor
  Exit processor
  Enquiry processor
Deduct highest fare on entry
Rebate difference on exit
Bonus point scheme

## Slide 18: Enquiry Terminal
Details of last and up to 10 transactions
Multi-language Chinese/English

## Slide 19: Portable Card Analyser (PCA)
Instant ticket inspection
Facility for printing violation receipt

## Slide 20: 7-Eleven
Integrated with Point-of-Sale system
7-Eleven network connects all stores

## Slide 21: Fast Food

## Slide 22: Vending
Vending - Swire CoCa Cola/ Vitasoy
Photos

## Slide 23: Access Control
Unique identification number for every Octopus card
Access premises
  Tierra Verde
  Waterfront
Controls door
Connected to Office PC for Access List Update

## Slide 24: On Street Parking Meters
Integrated into different types of parking meters
Data collected via handheld computer
May go wireless in the future

## Slide 25: Off Street Parking
Octopus payment at Shroff
Direct entry/exit using Octopus

## Slide 26: Add Value
Add Value Machines at stations
Customer service outlets
7-Eleven stores
Autopay
  Dah Sing Bank
  Standard Chartered Bank

## Slide 27: System Architecture
Four inter-connected layers
    Central Clearing House System (CCHS)
    Service Providers’ Central Computer (SPCC)
    Local Data Processing (LDP)
    Octopus Processor

## Slide 28
Frame Relay Network
Backup
Server
Sun ULTRASparc Server
LDP
SPCC
CCHS
Sun Workstations
Frame Relay
KCR
HYF
MTR
CTB
LRT
Fiber Optic
Gates
AVM
Octopus Processor
KMB
Fig 1- Octopus System

## Slide 29: Systems
Sun SPARC machines
Unix operating system
TCP/IP network
Frame relay links
Proven technology

## Slide 30: Data Consolidation
Creative Star Database
Seq No. Date Time Amt SP RV Last AV Device
100 01/2/99 12:05 -$3.7 MTR $197.5 091234
099 31/1/99 13:15 +$100.0 MTR $201.2 091234
098 28/1/99 19:05 -$3.7 MTR $101.2 094567
097 26/1/99 17:00 -$8.9 KMB $104.9 094567
096 25/1/99 18:20 -$9.9 MTR $113.8 094567
095 24/1/99 17:20 -$8.9 KMB $123.7 094567
094 24/1/99 08:53 -$9.9 MTR $132.6 094567
093 23/1/99 17:00 -$7.5 KMB $142.5 094567
092 23/1/99 08:20 -$9.9 MTR $150.0 094567
091 22/1/99 18:52 -$9.9 MTR $159.9 094567
MTR Database
Seq No. Date Time Amt RV Details AV Dev
100 01/2/99 12:05 -$3.7 197.5 Wanchai->Central 091234
099 31/1/99 13:15 +$100.0 201.2 Kowloon Bay 091234
098 28/1/99 19:05 -$3.7 101.2 Central->Wanchai 094567
096 25/1/99 18:20 -$9.9 113.8 Wanchai->Mongkok 094567
094 24/1/99 08:53 -$9.9 132.6 Mongkok->Wanchai 094567
092 23/1/99 08:20 -$9.9 150.0 Mongkok->Central 094567
091 22/1/99 18:52 -$9.9 159.9 Central->Mongkok 094567
KMB Database
Seq No. Date Time Amt RV Details AV Device
097 26/1/99 17:00 -$8.9 104.9 Route 115 094567
095 24/1/99 17:20 -$8.9 123.7 Route 105 094567
093 23/1/99 17:00 -$7.5 142.5 Route 104 094567

## Slide 31: Acquirer Interface
Central Clearing House System
Acquirer
Service Providers
Reports
Through SP’s network
Different types of Octopus Processor
or

## Slide 32: Future Plans
All transport applications
High-volume, low-value transaction businesses
Strategic partnerships for development of wider applications
Hybrid Cards
  Octopus + credit/debit card
  Contactless and Contact on same card

## Slide 33: Conclusion
Bring convenience to the public
Bring benefits to service providers
Reliable and fast payment
Low cost operations

## Slide 34
The Octopus – Thank You